## Slide 1
CPU
I-CACHE
D-CACHE
CORE
PROGRAM
AND
DATA MEMORY
PTAG MEMORY
MEMORY BLOCK
PTAG
PTAG-GEN
CMP
PTAG BUS
ON-CHIP
DATA BUS
ADDRESS BUS
SEC-ENG
BUS-HDLR
ADDRESS PTAG BUS
PMMU
FUZZY EXTRACTOR
(B)
(D)
(G)
(A)
(F)
(E)
(H)
(I)
(A) The BUS HANDLER (BUS-HDLR) provides memory block concatenated with physical address to the PTAG GENERATOR (PTAG-GEN).
(B) Fuzzy Extractor serves an extracted PUF-based key to PTAG-GEN. (C) The PTAG MEMORY MANAGEMENT UNIT (PMMU) can either provide:
(i) a chunk of PTAGs concatenated with their address location; (ii) or a time stamp for PTAG-GEN. (D) PMMU receives a new PTAG when it requests generation to PTAG-GEN.
(E) PTAG-GEN provides PTAG for comparison. (F) PMMU provides PTAG for comparison.
(G) If the comparison fails, a signal is sent to BUS-HDLR for action.
(H) PMMU sends and receives PTAGs from the PTAG Memory. (I) PMMU decodes virtual PTAG address to physical address and sends it to PTAG Memory.
(C)